## Slide 1
Guocong Zhai1, Kun Xie1*, Hong Yang1, and Di Yang2, * E-mail: kxie@odu.edu
1 Old Dominion University (ODU), 2 Morgan State University
Assessing the Safety Performance of Ride-hailing Services and Taxis: A Multivariate Spatial Approach with Exposure Uncertainty
Challenges
Background
Results & Discussions
The work is partially funded by the Transportation Informatics Lab, Department of Civil and Environmental Engineering at Old Dominion University (ODU).
Uncertainty of mode-specific exposures of ride-hailing services and taxis.
Spatial correlations across crash observations.
Inherent correlations among different types of crashes.
Data
Exposure Estimation
Methodology
Poster session 2096
Poster number: TRBAM-24-00486
Assess the safety performance of ride-hailing services and taxis.
Mode-specific exposure estimation with classical measurement errors.
Multivariate spatial approach simultaneously capturing spatial and inherent correlations.
Ride-hailing services are found to be prone to a higher risk of minor injury crashes compared with taxis, despite no significant difference between the risks of severe injury crashes
Objective
The full text is available in Accident Analysis & Prevention.
QR code::
Conclusions
Acknowledgements
Safer Mode?
Variables | Severe ride-hailing crashes |  | Minor ride-hailing crashes |  | Severe taxi crashes |  | Minor taxi crashes | 
 | Mean | SD | Mean | SD | Mean | SD | Mean | SD
Intercept | -8.49* | 0.80 | -6.61* | 0.81 | -9.06* | 0.84 | -6.53* | 0.72
Transportation factors |  |  |  |  |  |  |  | 
Ln (VMT) | 0.30* | 0.05 | 0.22* | 0.05 | 0.31* | 0.05 | 0.29* | 0.05
Ln (mode-specific VMT) | 0.11* | 0.03 | 0.17* | 0.03 | 0.10* | 0.03 | 0.07* | 0.03
Traffic signal number | 0.02* | 0.01 | 0.02* | 0.01 | 0.02* | 0.01 | 0.03* | 0.01
Land use factors |  |  |  |  |  |  |  | 
Number of education sites | 0.12* | 0.04 | 0.08* | 0.04 | 0.08* | 0.04 | 0.09* | 0.04
Number of alcohol-related sites | 0.05* | 0.02 | 0.07* | 0.02 | 0.05* | 0.02 | 0.06* | 0.02
Demographic factors |  |  |  |  |  |  |  | 
Median household income | 0.08* | 0.03 | 0.05* | 0.03 | 0.10* | 0.03 | 0.10* | 0.03
Transit ratio | 1.30* | 0.52 | 1.08* | 0.45 | 1.09* | 0.52 | 1.06* | 0.44
Walk ratio | 0.84 | 0.82 | 1.38* | 0.65 | 3.38* | 0.73 | 1.90* | 0.66
Models | Crash types | Ln (mode-specific VMT) |  | T test p-value
 |  | Mean | SD | 
NB | Severe ride-hailing crashes | 0.14 | 0.06 | 0.30
 | Severe taxi crashes | 0.07 | 0.03 | 
 | Minor ride-hailing crashes | 0.26 | 0.03 | < 0.01
 | Minor taxi crashes | 0.05 | 0.02 | 
MVCAR | Severe ride-hailing crashes | 0.12 | 0.03 | 0.86
 | Severe taxi crashes | 0.11 | 0.03 | 
 | Minor ride-hailing crashes | 0.16 | 0.03 | 0.03
 | Minor taxi crashes | 0.08 | 0.02 | 
MVCARME | Severe ride-hailing crashes | 0.11 | 0.03 | 0.81
 | Severe taxi crashes | 0.10 | 0.03 | 
 | Minor ride-hailing crashes | 0.17 | 0.03 | 0.02
 | Minor taxi crashes | 0.07 | 0.03 | 
Multivariate Conditional Autoregressive Model with Measurement Error (MVCARME)
K-dimensional multivariate normal distribution to capture spatial and inherent correlations
Gaussian distribution to identify measurement errors